## Slide 1: B4 – a 4 cycle barrel processor
Between GPUs and FPGAs in core efficiency
HUGE on-chip memory; in the gigabyte range
  Dynamic memory, needs memory process
  Around half DRAM, half fabric + computation
Divergent control flow at full speed, not SIM(T/D)
Designed for swarm intelligence and tracing sparse voxel octrees
Perfect for pipeline / pipegraph processing (as long as it fits on chip)
  Raytracing
  Deep learning
  Computational photography

## Slide 2: Simple Processor & Fabric + Lakes of Memory
Core has memory-like metal complexity and clocks
  4KB local memory
  64KB global memory
  16 bit barrel ALU
    Configurable: 4x16 bit threads, 2x32 bit threads or 1x64 bit thread
  8 thread contexts
Extremely high energy efficiency
  Massively reduced data movement
  Low clocks and voltages
Direct processing in memory
  Rather than 16Gbit DRAM in ~100mm^2, get 8Gbit DRAM + 16k cores

## Slide 3
Mostly memory
Mostly logic
Mostly wires
Local resources
Shared resources
Memory lanes (~20x)
Memory lanes (4x~20)
Link lanes (~76x)
Local lanes (~100x)
R ~16kb single port
L ~1kb single port
C 4-cycle barrel
X routing crossbar
A(C+L+links+X) < A(R)
16 bit ALUs
.. 2 slots chain to 32bit
.. 4 slots chain to 64bit
Throughput stays mostly equal between 16/32/64 modes,
1 active thread in 64bit,2 in 32bit, 4 in 16bit
Double width accumulator
FP support ~half speed of integer
(try for full speed, not at the cost of failing the area principle)
L is instruction and register store
  Each bank can I/O their link per cycle
R is “local” memory, but:
  4 nearest neighbours R’s used
  4x capacity, 4x bandwidth, 1.5x latency
Link lanes address near nodes with packets
  Dynamic or static routing, limited range
    Forwarding contexts to reach whole chip
8 contexts, 4 simultaneous at quarter clock
2 quarter clocks to switch running context
No registers. Multiple stacks per context
Streams (like memory) accessed as full stacks
  “write stack X to address Y”
  “stack X to core Y, context Z, stack W”
  “fetch Z words from Y to stack X”
  Potential for more complex ops…
Very compact, sort of dual issue stack ISA
  Optionally push a constant
  Stack(0) op Stack(1)
R
L
C1
R
L
C2
R
L
C0
R
L
C3
link
link
link
link
Lx
Lx
Rx
Lx
Rx
Rx
Rx
Lx
C0 – decode
C1 – execute 1
C2 – execute 2
C3 – commit
R0head – local Xbar
R1head – remote Xbar
R2head – access 1
R0tail – access 2
R1tail – remote Xbar
R2tail – local Xbar
for reads,
head is once
tail repeated
for burst access;
write is the other
way around
X